## Slide 1: Lot/Signal (Choose One) Investigation Summary
Problem Statement | 
Tech (s) / LotID (s) / WaferID (s) | 
Fail Characteristics Signal regionality Failing Parameter PreLM Test Performance | 
FA Submissions | 
Use this page like an abstract. Provide an overview of the signal, failing parameters, regionality, what is the total impact (# of lots, wafers, sites).
Once the BLIPS is closed, return to this page and describe what was learned: what was the PoC? Root cause? Actions taken by scrap owner?

## Slide 2: Additional charts

## Slide 4
REASON FOR ASSIGNING TO THIS TECH CENTER
FILL IN SECTION PERTAINING TO 80% CONFIDENCE GUIDELINE USED TO DETERMINE ASSIGNMENT:
(Minimum of 1 match for 80% confidence)
CHECK BOX | 80% CONFIDENCE GUIDELINES | COMMENTS
 | INTEGRATION/ TECHNOLOGY / TEST | PROBLEM SOVLING OWNER:
 | FA AVAILABLE ON SAMPLE IDENTIFYING PoC | FA#
 | FabGuard | 
 | RCA REPORT : REVIEW WEXIS COMMENTS, ABORTS, HOLDS, REWORK, etc | 
 | MULTIPLE LOTS - IDENTIFY COMMON TOOLS OVER TIME (NOT SEQUENTIAL) | 
 | SECONDARY PARMS (ex: device parametrics) | Based on FEOL FET / Res. Truth Table
 | REVIEW BOAT MAP MATCHES TOOL CONFIGURATION | 
 | SCRAP & DNA FAIL PARETO (FA HISTORY - LAST 6 months) | 
 | PROCESS INFORMATION MATCHING CURRENT EVENT AND ROOT CAUSE. ex( brookside, bess logs, etc) | 
 | SIGNATURE AND DATA SUPPORT 2 LIKELY TECH CENTERS - SPLIT SCRAP BETWEEN 2 TC'S | 
End |  | 

## Slide 5: FEOL FET/Resistor Scrap Various DNA Strings and High Level POC
NFET Tox Inversion, PFET Tox Inversion, ToxGL
ESIG = Gate Oxide Thickness
Tool = Gate Oxide Furnace, $HPFU - probably more lots in a tube.
DG / TG Tox Inversion = SG/Thin Tox Inversion electrical Values
Tool = DG / TG Track Apply (Photo)
NOT FEOL FET/Resistors: NPN Parameters (PNP = ), VBD/WLR Parameters (PNP = ) PC-Si , Gate Oxide Shorts, other defect parms (PNP = )
NFET Lpoly, PFET Lpoly (usually not WAC fails)
ESIG = Lpoly
Check with INTG. Is PC_CD within 1.5 sigma of target? If yes -- INTG & send email to Integration If no - INTG helps with POC based on PC_CD results
NFET Coverlap, PFET Coverlap (NOT VBD; usually not WAC fails): ESIG = Overlap Cap
NFET or PFET only; with VTLin = Well Implant NFET & PFET Cov with OPRS = S/D RTA Everything else: Spacer Dep or Spacer Etch
NDiffusion OPRS, PDiffusion OPRS, N Poly OPRS, P Poly OPRS: ESIG = DIFFUSION or POLY RESISTORS
Is there a spot or is the entire wafer bad? If 1-2 sites = OP spot = POLY RESISTORS. Need OP Spot designator - INTG? Is it N OPRS & P OPRS? = S/D RTA
Only N or P (not both) = BN or BP Implant
Everything Else = VTSat, IDSat, VTLin, BVDS, Ron, IDLin, GMds, etc...
On list of systematics = INTG = need to make this list Check WEXIS/HOLDS & REQD in detailed lot history - was there an abort or requeue in implant, spacer, RTA? Don’t rule out a misprocessed lot/improper recovery.
Is both NFETs & PFETs? If Lpoly moves too = PC Etch; If Tox moves too = Gate oxide If OPRS moves too = RTA; Use the boxes on the left for ESIG & Tool assignments.
else use FET PERFORMANCE & scrap to Spacer 2 Dep.
Is it NFET only? “FET PERFORMANCE” Check for requeues at NFET implant levels. (BF, NR, NV, etc) Check VTSat, IDSat, VTLin, and what features move. (HVT, DG only, etc) Is there a common implant between them? -- scrap to that implant. If VTLin Moves = Well Implanter If VTLin doesn’t move = Halo implant (1-3w); Extension Implant (4+ wafers).
Is it PFET only? “FET PERFORMANCE”
Check for requeues at PFET implant levels. (NW, PR, PV, etc) Check VTSat, IDSat, VTLin, and what features move. (HVT, DG only, etc) Is there a common implant between them -- scrap to that implant. If VTLin Moves = Well Implanter If VTLin doesn’t move = Halo implant (1-3w); Extension Implant (4+ wafers).

## Slide 6: Lot Investigation Summary 1 of 2
Investigation | Criteria for Success | Findings
Lot History Rework Process history(WEXIS/Fab Events/QC) - Holds/Requeues | Green: No unique events Yellow: Abnormal events noted, not of significance Red: Abnormal events needing additional investigation | 
Slot Maps | Green: Slot maps available, no patterns noticed Yellow: No Slot maps available Red: Slot maps available, interesting pattern found (Odd/even, One/Three, Front->Back, 1st/last wafer ,etc | 
CFM (for defect signals) | Green: Maps do not resemble fail signature Yellow: No PLY data Red: Maps resemble fail signature | 
Tool Alarms / Fabguard Review Depl Page, Fabguard, etc | May require 'deep dive' by Tool/Process Owner for Fabguard Raw data review. | 
Tool/Process/Integration Slides (as applicable) | Check Feature Dependency, I.e HP/HA NPN, Dual/Single MIM, Kx resistor, etc etc. | 
Queue Time | Green: No Operations > 3σ Yellow: Operations > 3σ, but time within historical baseline Red: Operations > 3σ, and time outside historical baseline | 
Other Findings | Red: Something else of interest Found | 
Next Steps (Actions with dates and owners for all fails) |  | 

## Slide 7: Lot Investigation Summary 2 of 2
Investigation | Criteria for Success | Findings
Similar Historical Events | Can ECM number be added to member last updated history? How to Query route changes in SiView/ECM? | 
Pattern Density | Is pattern density of affected level different from 'baseline' | 
Wafer Substrate | Is Substrate Supplier different vs 'base'. Trend by Wafer Supplier in Shiny | 
Process Changes in Sector and Prior/Subsequent Sector | Review with PI/Module/Char Team | 
Tool Diet | Check Tool Diet Prior to Running Affected Lot at 'Critical' tools to check for unusual processing | 
Maintenance History of Tool | Best source is IOI tool maint history or Fabview. | 
Tool Type Dependency | Opportunities: how to look up mixed deployment (non-PNL/PNL, WAC vs. Non-WAC etch, Ta/TaN Liner, Purion vs. Non-Purion implant, Westech/Ebara, 400's/600's testers, XT/Classic Cu-plating, HPT chuck type, twinscan vs. Asml vs. Nikon, MUV/DUV, 2300/9608) | 

## Slide 8: BACKUP

## Slide 9: Bad Lot Investigation & Problem-Solving (BLIPS) Expectations
Investigations started same day of signal when >= 3 wafers potentially scrapped after retest or FA submitted
  Includes lots that show potential changing signal, unless previously proven and known cause
  >= 3 wafers scrapped shown at DOM the following day

## Slide 10: Title - edit & clarify document name
If Bad Lot investigation requires Problem solving Allows a quick view of present understanding
Move to beginning of document Once Root Cause and CA/PA are identified
Issue:
Characterize Problem:
Impact:
Team:
Process Containment:
Point of Cause/Understanding:
Root Cause:
Corrective/Preventative Actions:

## Slide 11
Leader |  | Module/Area |  |  |  | Tool ID |  |  |  |  | F9 Event Standard |  |  | 
Problem Statement |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Exposure |  |  | Time to Detect |  |  |  |  |  | Total Time to React |  |  |  |  | 
Impact |  |  |  |  | # Lots On Hold |  |  |  |  |  |  | Recurrence Y/N |  | 
NPI and OTD Lots |  |  |  |  | # Lots Contained |  |  |  |  |  |  | Planned MRB Date |  | 
Point of Cause |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Detection Opportunity |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Problem and Product Containment Stop the bleeding | Action |  |  |  |  |  |  |  |  | Owner |  | Date | Date | 

## Slide 12
DOM File Link: Fab 9 Daily Operational Meeting Rev 3.pptx (sharepoint.com)